## Slide 1
SparseP
Towards Efficient Sparse Matrix Vector Multiplication
on Real Processing-In-Memory Architectures
Christina Giannoula
Ivan Fernandez, Juan Gomez-Luna,
Nectarios Koziris, Georgios Goumas, Onur Mutlu
20 December 2022

## Slide 2
Our Work
Efficient Algorithmic Designs
The first open-source Sparse Matrix Vector Multiplication (SpMV) software package, SparseP, for real Processing-In-Memory (PIM) systems
Extensive Characterization
The first comprehensive analysis of SpMV on the first real commercial PIM architecture
Full Paper: https://arxiv.org/pdf/2201.05072.pdf
Recommendations for Architects and Programmers
SparseP: https://github.com/CMU-SAFARI/SparseP
SparseP is Open-Source

## Slide 3
Sparse Matrix Vector Multiplication
Sparse Matrix Vector Multiplication (SpMV):
Widely-used kernel in graph processing, machine learning, scientific computing …
A highly memory-bound kernel
Operational Intensity
Performance
Peak Compute Performance
Peak Memory Bandwidth
SpMV
Roofline Model

## Slide 4
Real Processing-In-Memory Systems
Real Near-Bank Processing-In-Memory (PIM) Systems:
High levels of parallelism
Low memory access latency
Large aggregate memory bandwidth
Host CPU
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Main Memory
DRAM Bank
DRAM Bank
DRAM Bank
DRAM Bank
Bus

## Slide 5
Real Processing-In-Memory Systems
Real Near-Bank Processing-In-Memory (PIM) Systems:
High levels of parallelism
Low memory access latency
Large aggregate memory bandwidth
Host CPU
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Main Memory
DRAM Bank
DRAM Bank
DRAM Bank
DRAM Bank
Bus
Kwon+, [ISSCC 2021]
Lee+, [ISSCC 2022]
https://www.upmem.com

## Slide 6
SparseP: SpMV Library for Real PIMs
Our Contributions:
Design efficient SpMV kernels for current and future PIM systems
  25 SpMV kernels
    4 compressed matrix formats (CSR, COO, BCSR, BCOO)
    6 data types
    4 data partitioning techniques
    Various load balancing schemes among PIM cores/threads
    3 synchronization approaches
Provide a comprehensive analysis of SpMV on the first commercially-available real PIM system
  26 sparse matrices
  Comparisons to state-of-the-art CPU and GPU systems
  Recommendations for software, system and hardware designers

## Slide 7
Outline
SpMV Kernels for Real PIM Systems
Key Takeaways from Our Study
Conclusion

## Slide 8
SpMV Execution on a PIM System
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank

## Slide 9
Data Partitioning Techniques
1D Partitioning
=
1x output vector
*
4x input vector
Core 1
Core 2
Core 3
Core 4
perform the complete
SpMV computation
only on PIM cores
2D Partitioning
2x output vector
=
2x input vector
*
Core 1
Core 2
Core 3
Core 4
trade-off
computation vs
data transfer costs
SparseP supports two types of data partitioning techniques:

## Slide 10
1D Partitioning Technique
Load-Balancing Approaches:
CSR, COO:
  Balance Rows
  Balance NNZs *
BCSR, BCOO:
  Balance Blocks ^
  Balance NNZs ^
* row-granularity for CSR
^ block-row-granularity for BCSR

## Slide 11
1D Partitioning Technique
Load-Balancing of #NNZs:
CSR (row-granularity), COO
CSR
0
1
3
5
7
7
8
8
9
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowptr
colind
values
0
1
1
2
2
3
3
5
7
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowind
colind
values
COO
row-order
nnz-order
Core 1
Core 2
Core 3
Core 1
Core 2
Core 3
row-
granularity
nnz-
granularity

## Slide 12
1D Partitioning Technique
Load-Balancing of #NNZs:
CSR (row-granularity), COO
BCSR (block-row-granularity), BCOO
ΒCSR
0
1
3
5
7
7
8
8
9
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowptr
colind
values
0
1
1
2
2
3
3
5
7
0
2
5
3
5
3
6
4
4
2
1
8
3
6
9
3
4
7
rowind
colind
values
ΒCOO
block-row-order
block-order
Core 1
Core 2
Core 3
Core 1
Core 2
Core 3
block-row-
granularity
block-
granularity

## Slide 13
2D Partitioning Technique
Equally-Sized Tiles
output vector
+
Core 1
Core 3
Core 2
Core 4
4x
4x
2x
input vector
4x
4x
output vector
Core 1
Core 3
Core 2
Core 4
2x
input vector
+
output vector
+
Core 1
Core 3
Core 2
Core 4
3x
5x
2x
input vector
Equally-Wide Tiles
Variable-Sized Tiles
High NNZ imbalance
across PIM cores
High NNZ balance across PIM cores of the same vertical partition
High NNZ balance
across all PIM cores

## Slide 14
Load-Balance across Threads
Multithreaded PIM Cores:
DRAM
Bank
Multithreaded
PIM Core
Core 1
Core 2
Core 4
Core 3
Core 1
Core 2
Core 4
Core 3
1D Partitioning
2D Partitioning
Thread 2
Thread 1
Thread 2
Thread 1
Various load-balance schemes across threads
Balance #Rows
Balance #Rows

## Slide 15
Load-Balance across Threads
Multithreaded PIM Cores:
DRAM
Bank
Multithreaded
PIM Core
Core 1
Core 2
Core 4
Core 3
Core 1
Core 2
Core 4
Core 3
1D Partitioning
2D Partitioning
Various load-balance schemes across threads
Balance #NNZs
Balance #NNZs
Thread 2
Thread 1
Thread 2
Thread 1
(e.g., COO format)

## Slide 16
Load-Balance across Threads
Multithreaded PIM Cores:
DRAM
Bank
Multithreaded
PIM Core
Core 1
Core 2
Core 4
Core 3
Core 1
Core 2
Core 4
Core 3
1D Partitioning
2D Partitioning
Various load-balance schemes across threads
Various synchronization approaches among threads
Balance #NNZs
Balance #NNZs
Thread 2
Thread 1
Thread 2
Thread 1
(e.g., COO format)

## Slide 17
Synchronization Approaches
Multithreaded PIM Core:
Coarse-Grained (lb-cg)
Thread 1
Thread 2
Thread 3
=
output vector
Fine-Grained (lb-fg)
Thread 1
Thread 2
Thread 3
=
output vector
Lock-Free (lf)
Thread 1
Thread 2
Thread 3
=
output vector
+
=
+
Thread 1
partial results
DRAM Bank
Multithreaded
PIM Core

## Slide 18
SparseP Software Package
25 SpMV kernels for PIM Systems 
https://github.com/CMU-SAFARI/SparseP
Partitioning | Matrix Format | Load-Balancing
9x 1D Kernels | CSR | rows, nnzs *
 | COO▵ | rows, nnzs *, nnzs
 | BCSR | blocks ^, nnzs ^
 | BCOO▵ | blocks, nnzs
4x 2D Equally-Sized Tiles | CSR | --
 | COO▵ | --
 | BCSR | --
 | BCOO▵ | --
6x 2D Equally-Wide Tiles | CSR | nnzs *
 | COO▵ | nnzs
 | BCSR | blocks ^, nnzs ^
 | BCOO▵ | blocks, nnzs
6x 2D Variable-Sized Tiles | CSR | nnzs *
 | COO▵ | nnzs
 | BCSR | blocks ^, nnzs ^
 | BCOO▵ | blocks, nnz
Load-balance
across PIM cores/threads:
* row-granularity (CSR)
^ block-row-granularity (BCSR)
Synchronization
among threads of a PIM core:
▵ lb-cg, lb-fb, lf (COO, BCOO)
Data Types:
8-bit integer
16-bit integer
32-bit integer
64-bit integer
32-bit float
64-bit float

## Slide 19
Outline
SpMV Kernels for Real PIM Systems
Key Takeaways from Our Study
Conclusion

## Slide 20
UPMEM-based PIM System
20 UPMEM PIM DIMMs with 2560 PIM cores in total
Each multithreaded PIM core supports 24 threads
Host CPU
(2-socket,
Intel Xeon)
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
160 GB PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
128 GB Main Memory
DRAM Bank
DRAM Bank
DRAM Bank
DRAM Bank
Bus
DISPATCH
FETCH
ALU
MERGE
14-stage
Pipeline
24 KB
Instr. Mem.
64 KB
Data Mem.
DMA Engine
64 MB
DRAM
Bank
64
bits
24x
threads

## Slide 21
Sparse Matrix Data Set
26 sparse matrices*:
Diverse sparsity patterns
Variability on irregular patterns
Variability on block patterns
Regular Matrix
Scale-Free Matrix
* Suite Sparse Matrix Collection: https://sparse.tamu.edu/

## Slide 22
Kernel Execution on One PIM Core
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank

## Slide 23
16 threads, COO, 32-bit integer
Lock-Based Synchronization
Multithreaded
PIM Core
DMA Engine
DRAM
Bank
64
bits
UPMEM DRAM bank
Chart: Speedup
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
lb-cg | 1 | 1 | 1 | 1
lb-fg | 0.99601 | 0.99967 | 1 | 0.99978


Fine-Grained Locking: memory accesses to the local DRAM bank are serialized in the DMA engine of the UPEM PIM hardware.
Fine-grained locking (lb-fg)
does not improve performance over coarse-grained locking (lb-cg)

## Slide 24
16 threads, COO, 32-bit integer
Lock-Based Synchronization
Multithreaded
PIM Core
DMA Engine
DRAM
Bank
64
bits
UPMEM DRAM bank
Chart: Speedup
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
lb-cg | 1 | 1 | 1 | 1
lb-fg | 0.99601 | 0.99967 | 1 | 0.99978


Fine-grained locking approaches cannot improve performance over coarse-grained locking, when the PIM hardware does not support concurrent accesses to the local DRAM bank.
Key Takeaway 1
Provide low-cost synchronization support and hardware support to enable concurrent memory accesses to the local DRAM bank, and integrate multiple DRAM banks per PIM core to increase execution parallelism.
Recommendation 1

## Slide 25
16 threads, 32-bit integer
Load-Balance within a PIM Core
Chart: CSR
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
row | 1 | 1 | 1 | 1
nnz | 0.81818 | 1.2029 | 1.1059 | 1.5589
Chart: COO
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
row | 1 | 1 | 1 | 1
nnz-lb-cg | 0.68875 | 0.95256 | 1.0571 | 1.3718
nnz-lf | 0.86936 | 1.0307 | 1.0587 | 1.372
Load-balancing #NNZs
performs best in most matrices
Load-balancing #NNZ typically provides high computation balance across threads of a compute-limited PIM core

## Slide 26
16 threads, 32-bit integer
Load-Balance within a PIM Core
Chart: CSR
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
row | 1 | 1 | 1 | 1
nnz | 0.81818 | 1.2029 | 1.1059 | 1.5589
Chart: COO
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
row | 1 | 1 | 1 | 1
nnz-lb-cg | 0.68875 | 0.95256 | 1.0571 | 1.3718
nnz-lf | 0.86936 | 1.0307 | 1.0587 | 1.372
Load-balancing #NNZs
causes high row imbalance
Load-balancing #NNZs: one single thread performs a much higher #memory accesses and #synchronization operations than the rest

## Slide 27
16 threads, 32-bit integer
Load-Balance within a PIM Core
Chart: CSR
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
row | 1 | 1 | 1 | 1
nnz | 0.81818 | 1.2029 | 1.1059 | 1.5589
Chart: COO
| delaunay_n13 | wing_nodal | raefsky4 | pkustk08
row | 1 | 1 | 1 | 1
nnz-lb-cg | 0.68875 | 0.95256 | 1.0571 | 1.3718
nnz-lf | 0.86936 | 1.0307 | 1.0587 | 1.372
High operation imbalance in computation, synchronization, or memory instructions executed by multiple threads of a PIM core can cause high performance overhead.
Key Takeaway 2
Design algorithms that provide high load balance across threads of PIM core in terms of computations, synchronization points and memory accesses.
Recommendation 2

## Slide 28
32-bit integer
Scalability within a PIM Core
Chart: delaunay_n13
| 4 | 8 | 16 | 24 | #threads
CSR.nnz | 11.796 | 7.217 | 5.731 | 5.406
COO.nnz-lb-cg | 10.645 | 8.236 | 9.463 | 9.74
COO.nnz-lf | 10.499 | 7.433 | 7.319 | 7.159
BCSR.nnz | 23.811 | 14.44 | 11.696 | 11.433
BCOO.nnz | 23.615 | 14.181 | 11.274 | 10.969
Chart: wing_nodal
| 4 | 8 | 16 | 24 | #threads
CSR.nnz | 31.388 | 17.705 | 13.004 | 12.825
COO.nnz-lb-cg | 28.501 | 19.131 | 18.161 | 18.619
COO.nnz-lf | 28.009 | 18.125 | 16.755 | 16.533
BCSR.nnz | 116.676 | 59.845 | 40.704 | 40.637
BCOO.nnz | 118.02 | 60.853 | 41.548 | 41.219
Chart: raefsky4
| 4 | 8 | 16 | 24 | #threads
CSR.nnz | 238.6 | 130.331 | 100.285 | 100.239
COO.nnz-lb-cg | 211.448 | 126.62 | 114.52 | 114.436
COO.nnz-lf | 209.655 | 127.529 | 115.151 | 115.041
BCSR.nnz | 186.935 | 95.405 | 66.931 | 66.972
BCOO.nnz | 188.651 | 96.293 | 67.497 | 67.432
Chart: pkustk08
| 4 | 8 | 16 | 24 | #threads
CSR.nnz | 566.529 | 310.663 | 239.419 | 239.448
COO.nnz-lb-cg | 500.101 | 298.181 | 268.291 | 268.916
COO.nnz-lf | 494.797 | 299.871 | 268.378 | 268.455
BCSR.nnz | 622.99 | 329.885 | 218.288 | 206.107
BCOO.nnz | 631.83 | 337.386 | 220.508 | 207.754
Scalability increases up to 16 threads

## Slide 29
Kernel Execution on Multiple PIM Cores
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank

## Slide 30
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: Speedup
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 0.84396 | 6.8634
BCSR | 0.57691 | 0.45252
BCOO | 0.73399 | 6.1852
6.86x
13.66x
Core 1
In scale-free matrices, COO + BCOO provide higher non-zero element balance across PIM cores than CSR + BCSR, respectively.
Core 2
Core 1
Core 2
COO
CSR
(row-granularity)
1D
Scale-free: COO, BCOO 
10.26x CSR, BCSR

## Slide 31
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: Speedup
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 1.0236 | 1.2315
BCSR | 0.75497 | 0.60928
BCOO | 0.85746 | 0.944
1.23x
1.55x
In scale-free matrices, COO + BCOO provide higher non-zero element balance across threads than CSR + BCSR, respectively.
Core 1
Core 3
Core 2
Core 4
CSR
(row-granularity)
COO
Thread 1
Thread 2
Thread 1
Thread 2
2D Equally-Sized Tiles
Scale-free:
COO, BCOO 
1.39x CSR, BCSR

## Slide 32
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: 2D Equally-Wide Tiles
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 44.021 | 22.4092
BCSR | 1.1764 | 0.85832
BCOO | 46.4785 | 23.9397
Chart: 2D Variable-Sized Tiles
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 42.24 | 19.9686
BCSR | 1.1388 | 0.7889
BCOO | 40.0751 | 20.653
44x
42x
40x
46x
22x
24x
20x
21x
COO + BCOO formats provide higher non-zero element balance across PIM cores + threads than CSR + BCSR, respectively.
COO, BCOO  32.38x CSR, BCSR

## Slide 33
2048 PIM Cores, 32-bit integer
Comparison of Compressed Formats
Chart: 1D
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 0.84396 | 6.8634
BCSR | 0.57691 | 0.45252
BCOO | 0.73399 | 6.1852
Chart: 2D Equally-Sized
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 1.0236 | 1.2315
BCSR | 0.75497 | 0.60928
BCOO | 0.85746 | 0.944
Chart: 2D Equally-Wide
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 44.021 | 22.4092
BCSR | 1.1764 | 0.85832
BCOO | 46.4785 | 23.9397
Chart: 2D Variable-Sized
| regular matrices | scale-free matrices
CSR | 1 | 1
COO | 42.24 | 19.9686
BCSR | 1.1388 | 0.7889
BCOO | 40.0751 | 20.653
The compressed matrix format used to store the input matrix determines the data partitioning across DRAM banks of PIM-enabled memory. As a result, it affects the load-balance across PIM cores (and threads of a PIM core) with corresponding performance implications.
Key Takeaway 3
Design compressed data structures that can be effectively partitioned across DRAM banks, with the goal of providing high computation balance across PIM cores (and threads of a PIM core).
Recommendation 3

## Slide 34
End-to-End Performance
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank

## Slide 35
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
1D: #bytes to load the input vector grows linearly to #PIM cores
The scalability is limited by the load time

## Slide 36
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
The 1D-partitioned kernels are severely bottlenecked by the high data transfer costs to broadcast the whole input vector into DRAM banks of all PIM cores, through the narrow off-chip memory bus.
Key Takeaway 4
Optimize the broadcast collective collective in data transfers to PIM-enabled memory to efficiently copy the input data into DRAM banks in the PIM system.
Recommendation 4

## Slide 37
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
2D Equally-Sized: kernel time is limited by only
a few PIM cores assigned to the 2D tiles with the largest #NNZs
The scalability is limited by the kernel time

## Slide 38
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
2D Equally-Wide + 2D Variable-Sized:
high amount of zero padding to gather the output vector 
parallel transfers supported at rank granularity = 64 PIM cores
> 88% of data is zeros
The scalability is limited by the retrieve time

## Slide 39
COO format, 32-bit integer
Chart: 
| 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048 | 256 | 512 | 1024 | 2048
load | 0.80335 | 1.4839 | 1.7011 | 2.068 | 0.32437 | 0.5336 | 0.6043 | 0.72195 | 0.1249 | 0.22484 | 0.27172 | 0.32485 | 0.14916 | 0.25726 | 0.29956 | 0.42156
kernel | 0.1232 | 0.069691 | 0.040441 | 0.02752 | 0.47494 | 0.32395 | 0.20892 | 0.15895 | 0.10111 | 0.066658 | 0.04721 | 0.039679 | 0.085477 | 0.056677 | 0.041961 | 0.039371
retrieve | 0.073227 | 0.092414 | 0.07924 | 0.075744 | 0.11677 | 0.11317 | 0.082848 | 0.071002 | 0.62082 | 0.83822 | 0.80847 | 0.9204 | 0.60807 | 0.77084 | 0.77649 | 0.91829
merge | 0.00021704 | 0.00045044 | 0.00076661 | 0.0018127 | 0.083917 | 0.088973 | 0.080642 | 0.0865 | 0.15317 | 0.15585 | 0.15698 | 0.15005 | 0.1573 | 0.15688 | 0.15742 | 0.15753
1D
2D
Equally-Sized
2D
Equally-Wide
2D
Variable-Sized
#PIM Cores
#PIM Cores
#PIM Cores
#PIM Cores
Scalability
88.6%
88.0%
Optimize the gather collective operation at DRAM bank granularity in data transfers from PIM-enabled memory to efficiently retrieve the output results to the host CPU.
Recommendation 5
The 2D equally-wide and variable-sized kernels need fine-grained parallel data transfers at DRAM bank granularity (zero padding) to be supported by the PIM system to achieve high performance.
Key Takeaway 5

## Slide 40
COO format, 32-bit integer
Comparison of Sparse Matrices
Chart: 1D
| 64 | 128 | 256 | 512 | 1024 | 2048 | 64 | 128 | 256 | 512 | 1024 | 2048 | #PIM Cores | #PIM Cores
load | 0.63522 | 1.2729 | 1.2956 | 2.6626 | 3.2869 | 4.3862 | 0.20042 | 0.3428 | 0.60766 | 1.34 | 1.2257 | 1.584
kernel | 0.26478 | 0.1412 | 0.075047 | 0.042066 | 0.023897 | 0.014321 | 0.74798 | 0.38497 | 0.19828 | 0.10394 | 0.057887 | 0.032038
retrieve | 0.099986 | 0.11391 | 0.13471 | 0.15362 | 0.15231 | 0.13163 | 0.05155 | 0.063153 | 0.052537 | 0.084809 | 0.084989 | 0.071242
merge | 1.3109e-05 | 1.6386e-05 | 2.6217e-05 | 5.8989e-05 | 0.0001147 | 0.00026545 | 4.2463e-05 | 7.431e-05 | 9.5541e-05 | 0.00023355 | 0.00052017 | 0.0012527
hugetric-00202
ldoor
Best-performing = 64 PIM cores
Best-performing = 128 PIM cores
1D: #PIM cores that provides the best performance
depends on the sparsity pattern of the input matrix

## Slide 41
2048 PIM cores, COO format, 32-bit integer
Comparison of Sparse Matrices
Chart: 2D Equally-Sized
| 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | #Vertical Partitions | #Vertical Partitions
load | 0.9896 | 0.56616 | 0.33155 | 0.21588 | 0.11359 | 0.06027 | 0.96334 | 0.54181 | 0.27611 | 0.15187 | 0.10761 | 0.063194
kernel | 0.0020231 | 0.0047514 | 0.0049046 | 0.0097491 | 0.016434 | 0.030748 | 0.0082215 | 0.015168 | 0.015821 | 0.023109 | 0.044397 | 0.085049
retrieve | 0.0058979 | 0.013759 | 0.021313 | 0.044524 | 0.079326 | 0.13937 | 0.011342 | 0.01853 | 0.028485 | 0.054305 | 0.10038 | 0.1981
merge | 0.0024749 | 0.012037 | 0.01684 | 0.017076 | 0.032715 | 0.16773 | 0.017102 | 0.018266 | 0.038785 | 0.059923 | 0.11337 | 0.20792
Best-performing = 16 vertical part.
Best-performing = 8 vertical part.
2D: #vertical partitions that provides the best performance
depends on the sparsity pattern of the input matrix

## Slide 42
COO format, 32-bit integer
Comparison of PIM Systems
Chart: 2D Equally-Sized
| 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | #Vertical Partitions | #Vertical Partitions
load | 0.98757 | 0.5185 | 0.27327 | 0.15143 | 0.1056 | 0.057768 | 0.9896 | 0.56616 | 0.33155 | 0.21588 | 0.11359 | 0.06027
kernel | 0.0031119 | 0.0031698 | 0.0055837 | 0.0099542 | 0.018464 | 0.034435 | 0.0020231 | 0.0047514 | 0.0049046 | 0.0097491 | 0.016434 | 0.030748
retrieve | 0.0059459 | 0.01099 | 0.021514 | 0.036182 | 0.070873 | 0.12071 | 0.0058979 | 0.013759 | 0.021313 | 0.044524 | 0.079326 | 0.13937
merge | 0.0033674 | 0.010522 | 0.019668 | 0.019064 | 0.034186 | 0.15989 | 0.0024749 | 0.012037 | 0.01684 | 0.017076 | 0.032715 | 0.16773
PIM System A
hugetric-00202
PIM System B
hugetric-00202
Best-performing = 8 vertical part.
Best-performing = 16 vertical part.
System | PIM Cores | PIM Band. | Host CPU | Bus Band.
PIM A | 2048 @350 MHz | 1.43 TB/s | Intel Xeon Silver 4110 @2.1 GHz | 23.1 GB/s
PIM B | 2048 @425 MHz | 1.78 TB/s | Intel Xeon Silver 4215 @2.5 GHz | 21.8 GB/s

## Slide 43
COO format, 32-bit integer
Comparison of PIM Systems
Chart: 2D Equally-Sized
| 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | #Vertical Partitions | #Vertical Partitions
load | 0.98757 | 0.5185 | 0.27327 | 0.15143 | 0.1056 | 0.057768 | 0.9896 | 0.56616 | 0.33155 | 0.21588 | 0.11359 | 0.06027
kernel | 0.0031119 | 0.0031698 | 0.0055837 | 0.0099542 | 0.018464 | 0.034435 | 0.0020231 | 0.0047514 | 0.0049046 | 0.0097491 | 0.016434 | 0.030748
retrieve | 0.0059459 | 0.01099 | 0.021514 | 0.036182 | 0.070873 | 0.12071 | 0.0058979 | 0.013759 | 0.021313 | 0.044524 | 0.079326 | 0.13937
merge | 0.0033674 | 0.010522 | 0.019668 | 0.019064 | 0.034186 | 0.15989 | 0.0024749 | 0.012037 | 0.01684 | 0.017076 | 0.032715 | 0.16773
PIM System A
hugetric-00202
PIM System B
hugetric-00202
Best-performing = 8 vertical part.
Best-performing = 16 vertical part.
2D: #vertical partitions that provides the best performance
depends on the underlying hardware characteristics

## Slide 44
COO format, 32-bit integer
Various Matrices and PIM Systems
Chart: 2D Equally-Sized
| 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | hugetric-0020 | memchip
load | 0.98757 | 0.5185 | 0.27327 | 0.15143 | 0.1056 | 0.057768 | 0.97325 | 0.49039 | 0.2564 | 0.14874 | 0.089717 | 0.060068
kernel | 0.0031119 | 0.0031698 | 0.0055837 | 0.0099542 | 0.018464 | 0.034435 | 0.0082494 | 0.015142 | 0.015908 | 0.023046 | 0.044245 | 0.083328
retrieve | 0.0059459 | 0.01099 | 0.021514 | 0.036182 | 0.070873 | 0.12071 | 0.010673 | 0.016749 | 0.025848 | 0.052951 | 0.097192 | 0.17867
merge | 0.0033674 | 0.010522 | 0.019668 | 0.019064 | 0.034186 | 0.15989 | 0.0078232 | 0.030471 | 0.027367 | 0.065725 | 0.10259 | 0.1883
Chart: 2D Equally-Sized
| 1 | 2 | 4 | 8 | 16 | 32 | 1 | 2 | 4 | 8 | 16 | 32 | hugetric-0020 | memchip
load | 0.9896 | 0.56616 | 0.33155 | 0.21588 | 0.11359 | 0.06027 | 0.96334 | 0.54181 | 0.27611 | 0.15187 | 0.10761 | 0.063194
kernel | 0.0020231 | 0.0047514 | 0.0049046 | 0.0097491 | 0.016434 | 0.030748 | 0.0082215 | 0.015168 | 0.015821 | 0.023109 | 0.044397 | 0.085049
retrieve | 0.0058979 | 0.013759 | 0.021313 | 0.044524 | 0.079326 | 0.13937 | 0.011342 | 0.01853 | 0.028485 | 0.054305 | 0.10038 | 0.1981
merge | 0.0024749 | 0.012037 | 0.01684 | 0.017076 | 0.032715 | 0.16773 | 0.017102 | 0.018266 | 0.038785 | 0.059923 | 0.11337 | 0.20792
#Vertical Partitions
#Vertical Partitions
Chart: 1D
| 64 | 128 | 256 | 512 | 1024 | 2048 | 64 | 128 | 256 | 512 | 1024 | 2048 | #PIM Cores | #PIM Cores
load | 0.63522 | 1.2729 | 1.2956 | 2.6626 | 3.2869 | 4.3862 | 0.20042 | 0.3428 | 0.60766 | 1.34 | 1.2257 | 1.584
kernel | 0.26478 | 0.1412 | 0.075047 | 0.042066 | 0.023897 | 0.014321 | 0.74798 | 0.38497 | 0.19828 | 0.10394 | 0.057887 | 0.032038
retrieve | 0.099986 | 0.11391 | 0.13471 | 0.15362 | 0.15231 | 0.13163 | 0.05155 | 0.063153 | 0.052537 | 0.084809 | 0.084989 | 0.071242
merge | 1.3109e-05 | 1.6386e-05 | 2.6217e-05 | 5.8989e-05 | 0.0001147 | 0.00026545 | 4.2463e-05 | 7.431e-05 | 9.5541e-05 | 0.00023355 | 0.00052017 | 0.0012527
hugetric-00202
ldoor
`PIM System A
`PIM System B
There is no one-size-fits-all parallelization approach for SpMV, since the performance of each scheme depends on the characteristics of the input matrix and the underlying PIM hardware.
Key Takeaway 6
Design adaptive algorithm that tune their configuration to the particular patterns of each input given and the characteristics of the PIM hardware.
Recommendation 6

## Slide 45
Up to 2528 PIM Cores, 32-bit float
1D vs 2D
Chart: 
| hgc | mc2 | pfm | rtn | rjt | ash | del | tdk | mem | amz | fth | wbg | ldr | psb | bns | wbs | in | pks | cmb | sxw | skt | ask | GM (1) | GM (2)
1D | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2D (equally-sized) | 1.1069 | 1.0513 | 1.369 | 1.0535 | 1.3571 | 1.4257 | 1.6339 | 1.4236 | 1.4165 | 1.2136 | 1.2889 | 1.368 | 1.2745 | 1.3837 | 1.3542 | 0.81272 | 0.35968 | 0.95352 | 0.87023 | 0.49709 | 0.87267 | 0.74493 | 1.3057 | 0.69507
1.45x
1.31x
regular
scale-free
>1100 Idle Cores
>2200 Idle Cores
Best-performing SpMV execution:
trades off computation with lower data transfer costs

## Slide 46
2528 PIM Cores, 32-bit float
1D vs 2D
Chart: 
| hgc | mc2 | pfm | rtn | rjt | ash | del | tdk | mem | amz | fth | wbg | ldr | psb | bns | wbs | in | pks | cmb | sxw | skt | ask | GM (1) | GM (2)
1D | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2D (equally-sized) | 1.1069 | 1.0513 | 1.369 | 1.0535 | 1.3571 | 1.4257 | 1.6339 | 1.4236 | 1.4165 | 1.2136 | 1.2889 | 1.368 | 1.2745 | 1.3837 | 1.3542 | 0.81272 | 0.35968 | 0.95352 | 0.87023 | 0.49709 | 0.87267 | 0.74493 | 1.3057 | 0.69507
1.45x
1.31x
regular
scale-free
1329 Cores
253 Cores
Expensive data transfers to/from PIM-enabled memory performed via the narrow memory bus impose significant performance overhead to end-to-end SpMV execution. Thus, it is hard to fully exploit all available PIM cores of the system.
Key Takeaway 7
Design high-speed communication channels and optimized libraries in data transfers to/from PIM-enabled memory, provide hardware support to effectively overlap computation with data transfers in the PIM system, and/or integrate PIM-enabled memory as the main memory of the system.
Recommendation 7

## Slide 47
SpMV Execution on Various Systems
Real PIM
System
bus
bus
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU
+
Load the
input vector
Execute
the kernel
Retrieve the
partial results
Merge the
partial results
1
2
3
4
Main Memory
DRAM Bank
DRAM Bank
bus
Main Memory
DRAM Bank
DRAM Bank
Host CPU
Execute the kernel
1
CPU System
GPU System
SMX2
SMX2
Load the
input vector
Execute the kernel
Retrieve
the final vector
1
2
3
GPU Global Memory
DRAM Bank
DRAM Bank
Host CPU
GPU Cores
bus
Main Memory
DRAM Bank
DRAM Bank

## Slide 48
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric

## Slide 49
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Only (COO, 32-bit float):
  CPU = 0.51% of Peak Perf.
  GPU = 0.21% of Peak Perf.
  PIM (1D) = 50.7% of Peak Perf.

## Slide 50
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Only (COO, 32-bit float):
  CPU = 0.51% of Peak Perf.
  GPU = 0.21% of Peak Perf.
  PIM (1D) = 50.7% of Peak Perf.
End-to-End (COO, 32-bit float):
  CPU = 4.08 GFlop/s
  GPU = 1.92 GFlop/s
  PIM (1D) = 0.11 GFlop/s

## Slide 51
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Energy (COO, 32-bit float):
  CPU = 0.247 J
  GPU = 0.051 J
  PIM (1D) = 0.179 J
PIM: 1.38x higher energy efficiency over CPU

## Slide 52
CPU/GPU Comparisons
System | Cores | Peak Performance | Bandwidth | TDP
CPU | Intel Xeon Silver 4110 | 660 GFlops | 23.1 GB/s | 2x85 W
GPU | NVIDIA Tesla V100 | 14.13 TFlops | 897 GB/s | 300 W
PIM | UPMEM 1st Gen. | 4.66 GFlops | 1.77 TB/s | 379 W
Processor-
Centric
Memory-Centric
Kernel-Energy (COO, 32-bit float):
  CPU = 0.247 J
  GPU = 0.051 J
  PIM (1D) = 0.179 J
Many more results in the full paper: https://arxiv.org/pdf/2201.05072.pdf

## Slide 53
Outline
SpMV Kernels for Real PIM Systems
Key Takeaways from Our Study
Conclusion

## Slide 54
Conclusion
SpMV is a fundamental linear algebra kernel for important applications (HPC, machine learning, graph analytics… )
SpMV is a highly memory-bound kernel in processor-centric systems (e.g., CPU and GPU systems)
Real near-bank PIM systems can tackle the data movement bottleneck (high parallelism, large aggregate memory bandwidth)
Key Contributions:
  SparseP : first open-source SpMV library for real PIM systems
  Comprehensive characterization and analysis of SPMV on the first real PIM system
  Recommendations to improve multiple aspects of future PIM hardware and software
SparseP: https://github.com/CMU-SAFARI/SparseP
Full Paper: https://arxiv.org/pdf/2201.05072.pdf
Our Work

## Slide 55
SparseP
Towards Efficient Sparse Matrix Vector Multiplication
on Real Processing-In-Memory Architectures
Christina Giannoula
Ivan Fernandez, Juan Gomez-Luna,
Nectarios Koziris, Georgios Goumas, Onur Mutlu
20 December 2022